## Slide 2: Circuit Symbols
V
Battery
Cell
Fuse
Resistor
LDR
Voltmeter
Ammeter
Variable resistor
Diode
Switch (open)
Bulb (lamp)
A
Thermistor
LED

## Slide 4: Current
Flow of electrons (number of coulombs per second)
Current (Amps) = Charge (Coulombs)
        Time (seconds)
I x t
Q
Notes: A coulomb would be a stupendous amount of unbalanced charge (two objects each with one coulomb of unbalanced charge of the same type, placed 1 m apart, would rip through thick concrete to get away from each other). But one coulomb of moving charge per second (i.e. one amp) in a circuit is not a particularly large amount, and can be achieved with a couple of batteries. The reason this is possible is that in a circuit the charge is not unbalanced – the negative charge moves but is always balanced by the stationary positive ions it is moving through, so that each section of wire is neutral overall.
This presentation begins with a definition of voltage, something which is often neglected or only mentioned in passing at GCSE level. Students are often simply taught the rules about voltage in series and parallel circuits without ever really understanding what voltage is. I have found, in teaching A* to B grade level students in Year 10, that circuits make more sense to them, and they do better in exam questions on circuits, if they have developed an understanding of voltage.

## Slide 6: Resistance and resistors
Voltage = current x resistance
V = IR
V = Voltage (V)
I = Current (A)
R = Resistance (Ohms, Ω)

## Slide 7: Resistance is measured in ohms (Ω)
Resistance (ohms) = Voltage (volts)
Current (amps)
What is resistance?
Ions in a metal/wire/component resist the passage of electrons passing through it. The more difficult it is for electrons to pass through the metal, the more resistance there is, and the more energy the electrons use trying to get through it.
R x I
V

## Slide 10
1. Connect the circuit as shown
2. Connect a lead from the negative side of the ammeter to the crocodile clip at the zero end of the ruler. Connect a lead from the other crocodile clip to the negative side of the battery. Use this lead as a switch to disconnect the battery between readings.
3. Decide the interval distance (eg 10cm) you will investigate and connect the first distance to be tested between crocodile clips A and B.
4. Measure the readings on the voltmeter and ammeter at this distance.
https://youtu.be/X9cAcsDmo8w
https://youtu.be/QHlIrtAcOAg

## Slide 16: Ohm’s Law
The current flowing through a resistor at a constant temperature is directly proportional to the voltage across the resistor. So…
If you double the voltage,
the current also doubles.
Most resistant
Least resistant
Which line is the most and least resistant component?
https://www.youtube.com/watch?v=2CA1mcYw3IQ

## Slide 17
Diode
Filament lamp
Resistance changes through different component
Ohmic resistor

## Slide 19: Non-Ohmic Components
A thermistor is a component whose resistance decreases when the temperature increases.
Useful in thermostats to control temperature
An LDR is a component whose resistance decreases as the light intensity that falls on it increases
Useful in nightlights to switch on lights when it is dark

## Slide 20
Potential difference (volts) | Current (amps) | Resistance (R = V/I) (ohms)
https://youtu.be/vnRQnp6limA

## Slide 26: Series Circuits Rules - Current
The same current passes through components in series with each other
If the current through the lamps is 0.12A, what is the current through the cell?
0.12A
0.12A
0.12A
0.12A

## Slide 27: Series Circuits Rules - Voltage
The total potential difference of the voltage supply in a series circuit is shared between the components.
If the potential difference of the cell is 1.2V and the potential difference of across one lamp is 0.8V, what is the potential difference across the other lamp?
0.4V
1.2V
0.8V
0.4V

## Slide 28: Series Circuits Rules - Resistance
The total resistance of components in series is equal to the sum of their separate resistances.
What is the total resistance if one lamp in series has a resistance of 2 and the other has a resistance of 3?
5
2
3

## Slide 29: Parallel Circuits Rules - Current
The total current through the whole circuit is the sum of the currents through the separate components.
A1
If ammeter A1 reads 0.4A and A2 reads 0.1A, what would A3 read?
0.3A
A2
A3
0.4A
0.1A
0.3A

## Slide 30: Parallel Circuits Rules – potential difference
For components in parallel, the potential difference across each component is the same.
If the potential difference of the cell is 6V, the potential difference across each lamp will also be 6V.
6V
6V
6V

## Slide 31: Parallel Circuits Rules – resistance
The total resistance of two (or more) resistors in parallel is less than the resistance of the smallest individual resistor.
I1 = V/R = 6/1 = 6A
I2 = V/R = 6/2 = 3A
I3 = V/R = 6/6 = 1A
Total current = 6+3+1 = 10A

## Slide 38: Direct Current
Voltage
Time
This current is found in batteries
The charge flows in one direction only

## Slide 39: Alternating Current
Mains electricity uses an alternating current.
This means that the current repeatedly reverses direction.
The UK mains supply being about 230 V.
It has a frequency of 50 Hz (50 hertz), which means it changes direction, and back again, 50 times a second.

## Slide 40: Alternating Current
Frequency (Hz) = 1 ÷ time period
Voltage
Time

## Slide 41: Direct current vs alternating current

## Slide 42: Frequency = 1/time period

## Slide 45
The three-pin plug

## Slide 46: Components of a plug and cable
Live wire (brown) – This carries the current to the appliance. Touching this can be deadly!
Neutral wire (blue) – This completes the circuit and is usually at 0V
Earth wire (green/yellow) – This ‘earths’ the appliance in case one of the wires touches the casing
Fuse – This stops the flow of current if it gets too high

## Slide 47: The Earth Wire
Many electrical appliances have metal cases. The earth wire creates a safe route for the current to flow through if the live wire touches the casing.
Some appliances (hairdryers, vacuum cleaners) don’t have an earth wire.
This is because they are DOUBLE INSULATED

## Slide 48: How does the Earth wire protect us from electric shock
Normally current comes in from the live and leaves through the neutral
If the live wire touches the metal casing, the Earth wire is used to conduct the current away
This will massively increase the current running through the fuse, the fuse melts and breaks the circuit

## Slide 51: Calculating Power
This is a very useful equation, it will help you working out the current through any appliance knowing the power. We can calculate power in two ways.
Power (watts) = Current (amps) x Potential Difference (volts)
Power (watts) = Current2 (amps) x Resistance (ohms)
2
R

## Slide 53: Calculating energy transferred
Energy transferred in a circuit can be calculated in 2 ways:
Energy (joules) = Charge (coulombs) x Potential Difference (volts)
Energy (joules) = Power (watts) x Time (seconds)
V x Q
E
P x t
E

## Slide 55
Transporting electricity
Step-Up Transformer
Step-Down Transformer
This is how our
National Grid
Works!!
INCREASES voltage
REDUCES current REDUCES energy loss INCREASES efficiency
Reduces voltage back down to 230V

## Slide 59
Van de Graaff generator

## Slide 60
When you rub two different insulated materials against each other they become electrically charged.
This only works for insulated objects.
Metals just conduct the charge
Charging by Friction
Remember it is ELECTRONS moving from one place to another

## Slide 61
Two charged rods of different materials will attract each other if they have a different charge.
Two rods made of the same material will repel each other due to having the same charge.
Like charges repel: unlike charges attract

## Slide 66: Electric fields